## Slide 1: ECE 671 – Lecture 9
Bridges and Link Layer Switches

## Slide 2: Network bridge
Layer-2 network system

## Slide 3: Local area networks
Layer-2 connectivity across multiple segments
  How to get from end-system 1 to end-system 6?

## Slide 4: Source routing bridge
Explicit route information in each frame
Bridges need to discover network structure
  Explorer packets
Pros? Cons?

## Slide 5: Transparent bridge
Bridge maintains filtering database
  Flooding used if destination unknown
Bridge learns network structure over time
  Traffic reveals source location
  Filtering database updated
Filtering database entries time out after a while

## Slide 6: What happens here?
End-system 1 sends to end-system 2

## Slide 7: Spanning tree protocol
Need to create loop-free routes between all nodes
  Tree is inherently loop-free
Create tree by selectively turning off interfaces

## Slide 8: Spanning tree protocol
In case of failures, inactive interfaces can be activated
  Interfaces are not physically turned off, but logically
How to create spanning tree?

## Slide 9: Spanning tree protocol
Idea:
  Determine root node of tree
  Determine shortest-path spanning tree from root
Exchange of HELLO messages
  Message contains:
    Transmitting bridge ID
    ID of bridge assumed to be root
    Length of best known path to root
Protocol
  Switches start out as root
    If message with smaller root ID is discovered, accept new root
  “Designated bridge” has shortest path to root on LAN
    Root broadcasts periodic HELLO
    Designated bridges forward HELLO on their LAN

## Slide 10: Spanning tree protocol
A
B
G
D
E
c
F
A
B
G
D
E
c
F
(a) broadcast initiated at A
(b) broadcast initiated at D
first construct a spanning tree
nodes then forward/make copies only along spanning tree

## Slide 11: Spanning tree: Creation
A
B
G
D
E
c
F
1
2
3
4
5
stepwise construction of spanning tree (center: E)
A
B
G
D
E
c
F
(b) constructed spanning tree
center node
each node sends unicast join message to center node
  message forwarded until it arrives at a node already belonging to spanning tree

## Slide 12: Timers
Entries in filtering database time out
  Timers need to be designed for constant overhead
Example: timing wheel

## Slide 13: Timers: Approach comparison
“Hashed and Hierarchical Timing Wheels: Data Structures for the Efficient Implementation of a Timer Facility”, Varghese and Lauck
START_TIMER
STOP_TIMER
PER_TICK
O(1)
Straight Fwd
O(1)
O(n)
Sequential
List
O(n)
O(1)
O(1)
Tree Based
O(log(n))
O(1)
O(1)
Simple
Wheel
O(1)
O(1)
O(1)
High memory requirement
Hashed
Wheel (sorted)
Hashed Wheel
(unsorted)
Hierarchical
Wheels
O(n) worst case
O(1) avg
O(1)
O(m)
O(1)
O(1)
O(1)
O(1)
O(n) worst case
O(1) avg
O(1)